## Slide 1: Electronic Devices Introduction
V Kumar
Email:vkumar52@iitism.ac.in
Tel.: Office: 5426
Mobile: 9431122030
ED Lect. 1

## Slide 2
Unit No. | Topics to be Covered | Lecture Hours | Learning Outcome
1 | Physics and Properties of Semiconductors: Band structure, Fermi distribution, Density of states, intrinsic and extrinsic semiconductors, carrier concentration at thermal equilibrium | 7 | Acquire an understanding of the semiconductor band structure and calculation of carrier concentrations
2 | Carrier transport phenomena: Carrier drift and diffusion, Generation and recombination, Minority carrier lifetime, Continuity equation, Solution of diffusion equations, Quasi Fermi levels, Hall effect | 7 | Develop an understanding about the carrier transport in semiconductors
3 | p-n junctions: Built-in potential, Depletion region, Electrostatics of p-n junction, Derivation of diode equations, Current voltage characteristics, Capacitance, Transient behavior, Junction breakdown, Metal semiconductor junctions, Ohmic contact, Schottky diode, Solar Cells, Photodiodes, LEDs and Laser Diodes | 8 | Understand the functioning of various pn junction and metal semiconductor junction devices and derive their characteristics
4 | Bipolar junction transistors: Transistor analysis, Frequency response and switching, Ebers-Moll model, small signal model (h equivalent), Deviations from the ideal behavior | 8 | Ability to derive the BJT characteristics and obtain their mathematical models
5 | MOS system, Electrostatics of MOS structure, Capacitance Voltage characteristics, MOSFET fundamentals, I-V characteristics and MOS models | 7 | Understand the fundamentals and characteristics of MOS devices
6 | State-of-the-Art MOS Technology: small-geometry effects, fin-FETs, ultrathin body FETs, ballistic transport, hot-electron effects. | 3 | Get an overview of MOS technology and recent developments of device features
Course Objective
The objective of the course is to develop an understanding of the device concepts and their operation that will be needed in a broad range of areas including modern semiconductor devices, circuit and VLSI design and engineering.
Learning Outcomes
Upon successful completion of this course, students will: acquire a basic knowledge of the physical characteristics, such as electronic structures and optical and transport properties of semiconductors develop the understanding of the physics and internal working of the basic solid state devices and derive their characteristics have appreciation of semiconductor technology and advanced devices
ourse Type | Course Code | Name of Course | L | T | P | Credit
DC | ECC201 | Electronic Devices | 3 | 1 | 0 | 11

## Slide 3
Textbook:
Solid State Electronic Devices, B. G. Streetman and S. K Banerjee, Pearson Education India (2015)
Reference Books:
2. Semiconductor Device Fundamentals, R, F, Pierret, Pearson (2006)
3. Integrated Electronics, J. Millman and C. Halkias,and C. Parikh, Tata
McGraw-Hill, 3RG ed., (2017)
4. Principle of Electronic Materials and Devices, S. O. Kasap, McGraw Hills, 3rd Ed (2006)
5. Semiconductor Physics and Devices, D. Neamen and D. Biswas, McGraw Hill Education (2017)
6. Semiconductor Devices, Physics and Technology, S. M. Sze and M. Lee, John Wiley & Sons (2015)
7. Fundamentals of Modern VLSI Devices, Y. Taur and T. H. Ning, Cambridge University Press (2016)
Weightage distribution of a course may now be done accordingly.
The suggested distribution is:
Mid Sem: 0
End Sem: 48 Remaining 52% marks includes 4 mandatory quizzes (40% to 52%) and assignment(s) if any(12% to 0%)
Recommended books

## Slide 4
Topics of Unit 1:
Topic:
Physics and Properties of Semiconductors:
Band structure,
Fermi distribution,
Density of states,
Intrinsic and extrinsic semiconductors,
Carrier concentration at thermal equilibrium

## Slide 5
Introduction: Physics and Properties of Semiconductors
Why we study Electronics? What is electronics?
Science: is an art of knowing the fact of the nature/ universe.
It is the study of the physical world and natural laws.
It is the study to discover the origin of life.
Physics: is the science that deals with matter & energy, and their interactions.
: the physical processes and phenomena of a particular system.
Electronics : Electronics is science (technology) of controlling energy by
movement of electrons. There will be moment (mv) loss.
Photonics: is science of controlling energy by movement of photons. Photons (Energy E = hᵞ) are mass-less and hence no momentum (mv) loss.
Optoelectronics: is science of controlling photon energy by movement of photons.
Instrumentation: is process of controlling various energy levels
and control energy exchanges.

## Slide 6
Electronic Devices: Provides students with a sound understanding of
existing devices.
It is a power tool to learn newly developed devices too.
Semiconductor (S/C) Device: is an electronic component that exploit the electronic props. of S/Cs (Si, Ga, GaAs, Alloys AlGaAS;
Organic S/Cs, and
graphene metal S/Cs= next generation technology)
to make as single desecrate device or an IC.
Properties of S/C conductivity (σ) can be controlled by an e .f., m.f., heat or doping

## Slide 7
Electromagnetic Spectrum:
X-ray 1018 | y-ray 1021 | Cosmic ray 1021
kHz3 MHz6 GHz9 THz12 OF14-15

## Slide 8
Type of Radiation | Frequency Range (Hz) | Wavelength Range
gamma-rays | 1020 - 1024 | < 10-12 m
x-rays | 1017 - 1020 | 1 nm - 1 pm
ultraviolet | 1015 - 1017 | 400 nm - 1 nm
visible | 4 - 7.5*1014 | 750 nm - 400 nm
near-infrared | 1*1014 - 4*1014 | 2.5 μm - 750 nm (Optical F)
infrared | 1013 - 1014 | 25 μm - 2.5 μm
microwaves | 3*1011 - 1013 | 1 mm - 25 μm
radio waves | < 3*1011 | > 1 mm

## Slide 9
Periodic Table: relevant part
Period | II | III | IV | V | VI
2 |  | B | C | N | O
3 | Mg | Al | Si14 | P | S
4 | Zn | Ga | Ge32 | As | Se
5 | Cd | In | Sn | Sb | Te
6 | Hg |  | Pb |  | 
Semiconductor : A S/C (Semi +conductor) is defined as a material whose conductivity lies between a conductor and insulator. Conductivity() , Resistivity () of some materials are shown below: (σ = 1/ ρ)
 | Insulators | Semicon-ductors | Conductors | Organic S/Cs | Graphene metal S/Cs
 (S/cm) | 10-18 – 10-8 | 10-8 - 104 | 104 - 106 |  | 
 (-cm) | 1018 - 108 | 108 – 10-4 | 10-4 – 10-6 |  | 

## Slide 10
Comparison of Physical properties of Graphene, Silicon (Si) and Copper (Cu)
Physical properties | graphene | Si | Cu
Melting Point (K) | 3800 | 1687 | 1357
Thermal conductivity ( ) | 5 | 0.15 | 0.385
Current density (A/) | > | - | >
Electron mobility () | >10000 | 1400 | -
Mean free path (nm) | 1x | 20 | 40
Young’s modulus | 1 TPa | 0.14 TPa | -
Tensile strength | 1100 GPa | 165 GPa | -
Band Gap | Zero | 1.10 eV (Indirect) | Zero
Physical properties | graphene | Si | Cu
Melting Point (K) | 3800 | 1687 | 1357
 | 5 | 0.15 | 0.385
 |  | - | 
 | >10000 | 1400 | -
Mean free path (nm) |  | 20 | 40
Young’s modulus | 1 TPa | 0.14 TPa | -
Tensile strength | 1100 GPa | 165 GPa | -
Band Gap | Zero | 1.10 eV (Indirect) | Zero

## Slide 11
Conduction Electrons in Pure (Si) Semiconductor
Si and Ge are 4th gp materials having 3-dimensional, diamond type, tetrahedral S/C (4 nos of valence electrons in the outermost orbit). The crystals are covalently bonded with the neighbouring atoms. Thy are weak-bond and broken due to thermal excitation and electron becomes free and function as charge carrier to conduction through crystal.

## Slide 12
Some of these Figures are from Brian Ackland, Stevens Institute of Technology, NJ

## Slide 13
If we introduce a boron (group III-acceptor) atom:
Can accept an extra electron which creates a hole –leads to a negative B─ ion
– but no conduction electron
– property of semiconductors: large changes in conductivity through the
addition of trace amounts of dopant material
Impure S/Cs or Doped S/Cs:
B B- + hole
in neighboring atom

## Slide 14
Replace one silicon atom with an arsenic (group V - donor) atom:
Contributes one extra electron which is weakly held
– free to wander at room temperature (almost 100% ionization)
– electron leaves behind a positive As+ ion – but no hole
As As+ + electron
majority

## Slide 15
ED Lect 2. (Ref. -Saleh & Teich)
Types of S/Cs and their Applications
Ref. -Saleh & Teich
Elementary, Binary, Ternary, and quaternary S/Cs

## Slide 20
  Elemental S/Cs: Si, Ge
  Eg = 1.11 0.66
  λg = 1.15 1.88
  Binary S/Cs:
  III-V binary S/Cs
  AlP AlAs AlSb
    Eg (eV) = 2.45 2.16 1.58
    λc (μm) = hᵞ/Eg (eV ) = 0.52 0.57(VIS) 0.75
  GaP GaAs GaSb
  Eg (eV) = 2.26 1.42 0.73
  λc (μm) =1.24/Eg = 0.55 0.87 (NIR) 1.70
  GaAs is the best S/C for the LED of Ist window of the O.F.
    InP InAs InSb

## Slide 21
Solid curve – D Gap
Dashed curve- I Gap

## Slide 22
II-VI | ZnO |  | 
 | ZnS | CdS | HgS
 | ZnSe | CdSe | HgSe
 | ZnTe | CdTe | HgTe
  II-V binary S/Cs

## Slide 23
(AlxGa1-x)As |  | Eg (eV) | λg (μm) | a (Ao )
x=0 | GaAs | 1.42 | 0.87 | 5.64
x=1↑ | AlAs | 2.16 | 0.57 λ↓ Blue Shift | 5.55
(GaxAl1-x)As |  |  |  | 
x=o | AlAs | 2.16 | 0.57 | 5.55
x=1 ↑ | GaAs | 2.42 | 0.87 λ↑ Red shift | 5.64
Inx Ga1-x AS |  |  |  | 
x=o | GaAs | 2.42 | 0.87 | 5.64
x=1↑ | InAs | 0.36 | 3.44 λ Red Shift | 
Ternary S/Cs: :

## Slide 24
Quarternary S/Cs
(In1-x Gax)(As1-yPy ):
Appls. :1.2 to 1.6 µm W/L LED

## Slide 25
 |  | Eg (eV) | λg (μm)
X=0=y | InAs | 0.36 | 3.44
X=1=Y | GaP | 2.26 | 0.55
(In1-x Gax)(As1-yPy )
Mixing ratio of x and y is y= 2.16 (1-x)
USED BETWEEN 1.1 - 1.6 µm W/L LEDs & PDs

## Slide 26
Energy Band in Solids
ED Lect 3: (Strretman + Kasap) .
What is meant by energy bands in solids?
An isolated atom possesses discrete energies of different electrons. ...
If 'N' number of atoms are brought together to form a solid (Ex: bricks/ stone pieces form wall, roof, road) and if these atoms' electrons interact and give 'N' number of closely spaced energy levels in the place of discrete energy levels, it is known as bands of allowed energies

## Slide 27
Ex.- C6 = 1S2 2sp2

## Slide 29
Ex. -Si14 = 3S2 3p2: As the distance b/w atoms approaches the equilibrium inter atomic distance of Si, i.e. d=a, the band splits in two bands separated by energy gap
CV
VB
Empty

## Slide 31
xxxxxxx

## Slide 32
LCAOs form Molecular orbitals

## Slide 33
Electronic Stru

## Slide 34
LCAO of 2 atoms

## Slide 35
LCAO of 2H atoms5

## Slide 36
LCAO of 3H atoms5

## Slide 37
Each

## Slide 38
Ex. of N Li3 (=1s2 2s1) atoms
free
As the distance b/w atoms approaches the equilibrium inter atomic distance of Si, i.e. d=a, the band splits in two bands separated by energy gap Eg

## Slide 42
Totally filled and totally empty bands do not allow current flow
Metal conduction band is half-filled
Semiconductors: Conductance dramatically increased through impurity doping
Lect 4

## Slide 43
Direct and Indirect Band gap1
Ex: DG- GaAs, GaSb, InAs, InP; Ex: IG- Si, Ge, AlP, AlS

## Slide 46
(AlxGa1-x)As |  | Eg (eV) | λg (μm) | a (Ao )
x=0 | GaAs | 1.42 | 0.87 | 5.64
x=1↑ | AlAs | 2.16 | 0.57 λ↓ Blue Shift | 5.55

## Slide 47
Up to X= 38% follow direct gap

## Slide 48
3.2.2 Effective Mass1
Mass of moving electron is known as effective mass. It is different than the rest mass or mass of electron.

## Slide 49
Find the (E, k) relationship for free electron and relate it to the electron mass1
From de Broglie relation, a moving electron in
a crystal with a wavelength λ, electron momentum p
is given by De Broglie relation as:
p = h/λ = h/(2π/k) = ђk
Also p = mv ,i.e., v= p/m
= ak2 Parabola
or m* ↑ =
Where, is curvature of the parabola . Effective mass increases with the decrease of curvature and vice versa

## Slide 50
N-type silicon has a donor energy level
- Donor ionization energy = Ec – Ed ≈ 50 meV
P-type silicon has an acceptor energy level
P- type and N-type Semiconductors

## Slide 51
Totally filled and totally empty bands do not allow current flow
Metal conduction band is half-filled
Semiconductors: Conductance dramatically increased through impurity doping

## Slide 53
Lect 5. Carrier Concentration1,5
Electrons in solids obey Fermi-Dirac statistics. However, classical particles (e.g.) obey Boltzmann statistics (atomic transition)

## Slide 54
The Fermi Energy1
Electrons in solids obey Fermi-Dirac statistics. However, classical particles (e.g.) obey Boltzmann statistics (atomic transition)
Fermi-energy is defined as energy of the top most filled level a absolute zero, i.e., T=0.
Fermi Dirac distribution function f(E) gives the probability that an available energy state at E occupied by an electron at absolute T.
Or
It tells the distribution of electrons over a range of allowed energy levels at
thermal equilibrium and given by the following relation:
where E is the energy state occupied by an electron at abs. Temp T,
k is the Boltzmann constant k = 8.62 x 10 -5 eV/K = 1.38 x 10 -23 J/K, and EF is called Fermi level and is an important quantity in the analysis of S/C behavior.

## Slide 55
1. At T=0 and
2. At T>0

## Slide 56
In the band theory, we have seen that when the distance b/w atoms approaches the equilibrium inter atomic distance of Si, i.e. d=a, the band splits in two bands separated by energy gap / forbidden energy gap

## Slide 57
Expo. decay

## Slide 58
Intrinsic semiconductor

## Slide 59
Fermi function for intrinsic and doped s/c
ef_psd

## Slide 60
Density of States

## Slide 61
Lect 6: Carrier concentration at thermal equilibrium (n0)
Since Fermi Dirac Distribution Function f(E) gives the probability that an available energy state at E occupied by an electron at absolute T. This helps us in calculating the electron and hole concs. in a S/C if densities of available states (DOSs) are known. We can write

## Slide 62
(c) p-type
(b) n-type
Holes
Electrons
(a) Intrinsic
dos N(E)
f(E)
Carrier concs

## Slide 70
Nc: Effective density of state at bottom of C.B.
Nv: Effective density of state at top of V.B.
Some useful forms

## Slide 71
Values of Nc and Nv for Si, Ge and GaAs at 300 K.
 | Si | Ge | GaAs
mn (x m0) | 1.08 | 0.89 | 0.067
mp (x m0) | 0.55 | 0.29 | 0.47
Nc (cm-3) | 2.82 x1019 | 2.10 x1019 | 4.32 x1017
Nv (cm-3) | 1.02 x1019 | 3.91 x1018 | 8.07 x1018
Do not take these numbers very seriously

## Slide 72
Lect 7. Fermi Level of Intrinsic Semiconductor

## Slide 73
Intrinsic Carrier Concentration
n*p is independent of EF
Law of mass action
ni for Si is approximately 1010 cm-3

## Slide 74
Fermi Energy for Extrinsic Semiconductors
Assume shallow donors  Complete ionization
 n = ND
Similarly, for holes

## Slide 75
Example
Si is doped with As 1016 cm-3.
Find carrier concentration and Fermi level at 300 K.
Assume ni = 1010 cm-3 ; Nc =1020 cm-3
Ec – EF = 0.23 eV
n=1016 cm-3 ; p = 104 cm-3

## Slide 76
Compensated Semiconductors
Both donor and acceptor impurities are present
Impurity with higher concentration determines the type of
conductivity
Fermi level must adjust to preserve charge neutrality
Using
Similarly

## Slide 77
Effect of Temperature on EF

## Slide 78
Carrier ionization: effect of temperature
Freeze-out region
Not all donor impurities ionized
Some electrons are frozen
Extrinisc region
All donor impurities ionized
Intrinsic region
Electrons excited from VB
Intrinsic carrier conc. Becomes
comparable to the donors

## Slide 79
Energy Momentum diagrams & Effective mass
Free Electrons:
Inside a s/c crystal:
: Electron effective mass
Similarly, for holes

## Slide 80
For (EF – E) >> kT

## Slide 81
Basic block of S/C devices
Metal-semiconductor interface;
p-n junction;
Heterojunction interface;
Metal-oxide-semiconductor structure.
Ack.: Ekapon, KMUTT